## Slide 1: CSCI-4320/6360: Parallel Programming & Computing DCC 308, Tues./Fri. 10-11:30 a.m. Introduction, Syllabus & Prelims
Prof. Chris Carothers
Computer Science Department
MRC 309a
Office Hrs: Tues/Fri, 11:30 a.m. – 1:30 p.m.
chris.carothers@gmail.com chrisc@cs.rpi.edu
www.cs.rpi.edu/~chrisc/COURSES/PARALLEL/SPRING-2018

## Slide 2: Let’s Look at the Syllabus…
See the syllabus on the course webpage.

## Slide 3: To Make A Fast Parallel Computer You Need a Faster Serial Computer…well sorta…
Review of…
  Instructions…
  Instruction processing..
Put it together…why the heck do we care about or need a parallel computer?
  i.e., they are really cool pieces of technology, but can they really do anything useful beside compute Pi to a few billion more digits…

## Slide 4: Single Processor/Core Performance Over Time
Processor clock rates and overall performance peaked in ~2005! Why?
From: “Computer Organization and Design: The Hardware/Software Interface”, Patterson and Hennessy, 2009

## Slide 5: “Laundry” Processor Design
Processor functions similar to doing laundry.
  Sort the clothes
  Wash a load of clothes
  Dry a load of clothes
  Fold a load of clothes
  Place clothes in cabinet
Processors operate on “instructions” instead of clothes
  E.g add two numbers and store result
Can do better than serial processing of steps!

## Slide 6: Pipeline “Laundry” Processing
Overlaps each step so you are done by 9:30 p.m. and not 2 a.m. !
Can do even better if 2+ washers and dryers are used ..
From: “Computer Organization and Design: The Hardware/Software Interface”,
Patterson and Hennessy, 2009

## Slide 7: Pipeline Processor Design
Fetch
Decode
Execute
Memory Access
Write result back
All stages of the pipeline are overlapped which vastly improves performance!
“Superscalar” pipelines issue and processor multiple instructions per clock cycle.

## Slide 8: CPU Power Consumption…
Typically, 100 watts is the limit..

## Slide 9: Single Processor/Core Performance Revisited
Golden age: Compiler + Architecture Innovations coupled with Moore’s Law
Exhausted instruction level parallelism (ILP), hit power wall and could not increase clock rate
Increased core count as new design point!

## Slide 10: Impact of Multicore on Supercomputers…
06/2007: #1 system is ~70x faster than #500
11/2013: #1 system is ~287x faster than #500
50% of total performance is achieved by top 17 of the Top 500 systems
Top 500 list over time(1993 – 2013): Green is Sum, Red is #1, Pink is #500
In 2013, AMOS @ 1 PF: #1 private academic institution in US, #4 among all US universities,
Jan. 2018, AMOS is #229 but still #1 among US private institutions
Notes: Say what Top500 list is.

## Slide 11: Multicores on Steroids: Accelerator and GPU cards
 | NVIDIA V100
Peak 64 bit FLOP rate | 7.8 TF
Memory Size | 16 GB
Memory Bandwidth | 900 GB/sec.
# of cores | 5,120
 | Intel Phi
Peak 64 bit FLOP rate | 1.2 TF
Memory Size | 16 GB
Memory Bandwidth | 352 GB/sec.
# of cores | 61
Intel Phi’s programming model is similar to AMOS.
The GPU (V100) execution model is a radical departure! Let’s see 

## Slide 12: Simple CPU Implementation of Reduce Operation
/* integer specific reduce on CPU */
int reduceCPU(int *data, int size)
{
int sum = data[0];
for (int i = 1; i < size; i++)
{
sum += data[i];
}
return sum;
}
17
23
8
19
62
12
141
data[]
sum

## Slide 13: NVIDA “CUDA” Implementation of Reduce Operation
template <unsigned int blockSize>
__global__ void reduce6(int *g_idata, int *g_odata, unsigned int n)
{
extern __shared__ int sdata[];
unsigned int tid = threadIdx.x;
unsigned int i = blockIdx.x*(blockSize*2) + tid;
unsigned int gridSize = blockSize*2*gridDim.x;
sdata[tid] = 0;
while (i < n) { sdata[tid] += g_idata[i] + g_idata[i+blockSize]; i += gridSize; }
__syncthreads();
if (blockSize >= 512) { if (tid < 256) { sdata[tid] += sdata[tid + 256]; } __syncthreads(); }
if (blockSize >= 256) { if (tid < 128) { sdata[tid] += sdata[tid + 128]; } __syncthreads(); }
if (blockSize >= 128) { if (tid < 64) { sdata[tid] += sdata[tid + 64]; } __syncthreads(); }
if (tid < 32) {
if (blockSize >= 64) sdata[tid] += sdata[tid + 32];
if (blockSize >= 32) sdata[tid] += sdata[tid + 16];
if (blockSize >= 16) sdata[tid] += sdata[tid + 8];
if (blockSize >= 8) sdata[tid] += sdata[tid + 4];
if (blockSize >= 4) sdata[tid] += sdata[tid + 2];
if (blockSize >= 2) sdata[tid] += sdata[tid + 1];
}
if (tid == 0) g_odata[blockIdx.x] = sdata[0];
}
~10x more complex to develop for 2-5x gain in performance.
// int specific reduce on CPU
int reduceCPU(int *data, int size)
{
int sum = data[0];
for (int i = 1; i < size; i++)
{
sum += data[i];
}
return sum;
}

## Slide 14: “AMOS”/MPI Implementation of Reduce Operation
int reduceAMOS(int *data, int size)
{
int sum = data[0];
int final_sum = 0;
MPI_Allreduce( &sum,
&final_sim,
size,
MPI_INT,
MPI_SUM,
MPI_COMM_WORLD );
return final_sum;
}
17
23
8
19
62
12
141
data[]
sum
“task”
…
T0
T1
TN
Reduce in Network
All “sum”s
final_sum
T0
T1
TN
…
Notes: Explain MPI task model first!!

## Slide 15: Supercomputers vs. Clouds
Supercomputer Systems:
  Fault tolerance via well designed hardware & “checkpointing” of state by app.
  Network: 20 GB/sec and < 5 usec latency
  Massive parallel filesystem
  Very power efficient system overall!!
  Job scaling to millions of cores!
  Custom network (e.g., BG/Q 5-D torus)
COTS “Cloud” Systems:
  Fault tolerance via replication of data via software - Hadoop/MapReduce
  Network: 1 to 5 GB/sec and ~500usec latency
  Client disks used like extended RAM memory which drives cloud design and performance
  Less power efficient system
  Job scaling limits to < 1,000 cores
  Commodity network (e.g., 1 Gb/sec Ethernet switch)
Notes: Giga == billions, Tera == trillions, Peta = Quadrillions and Exa == Sextillions

## Slide 16: What About Storage Devices?
Magnetic Hard Disk Drives
Solid State Storage (SSD) / NVMe
Platter
Spindle
Head
Actuator
LTO 6
2.5 TB, 160 MB/sec
Thanks to R. Ross, ANL and B. Welch, Google
Semi-conductor storage w/o any moving parts!
Magnetic Tape
Notes: Question: Why do we use tape? LTO == Linear Tape-Open which is an open standard developed in the 1990’s

## Slide 17: Disk Transfer Rates over Time
Thanks to R. Freitas of IBM Almaden Research Center for providing much of the data for this graph.
5 minutes to read 315 MB disk
At 1 MB/sec (IBM 3350)
25 minutes to read 440 GB disk
At 280 MB/sec (Cheetah @ 15K RPM)
7.4 hours to read 4 TB SATA
At 150 MB/sec
Large growing cap between storage and compute!!
Notes: 17

## Slide 18: Why can’t we move to FLASH ?
Storage Hierarchy is DRAM, SCM, FLASH, Disk, Tape
Cannot manufacture enough bits via Wafers vs. Disks
  SSD 10x per-bit cost, and the gap isn’t closing
  Cost of semiconductor FAB is >> cost of disk manufacturing facility
  World-wide manufacturing capacity of semi-conductor bits is perhaps 1% the capacity of making magnetic bits
    500 Million disks/year (2012 est) avg 1TB => 500 Exabytes (all manufacturers)
    30,000 wafers/month (micron), 4TB/wafer => 1.4 Exabytes (micron)
And Tape doesn’t go away, either
  Still half the per-bit cost, and much less lifetime cost
  Tape is just different no power at rest physical mobility higher per-device bandwidth (1.5x to 2x)
Thanks to R. Ross, ANL and B. Welch, Google

## Slide 19: Amdahl’s Law
The anti-matter to Moore’s Law..(cpu performance doubles every 24 months)
  Actually it is more about transistor counts…
The law states that given N processors and F is the faction of execution time that can be made parallel, then the amount of performance improvement (i.e., speedup) is:
          1/((1 – F) + F/N)
  Note as N  infinity, then speedup limited by
  1/(1-F)
  So, then what about supercomputers ….

## Slide 20: Titan - #5 on Top500 @ 27/17.49 PF
Architecture 18,688 AMD Opteron 6274 16-core CPUs +
18,688 Nvidia Telsa K20X GPUs
Power 8.2 MW
Space 404 m2 (4352 ft2)
Memory 710 TB (598 TB CPU and 112 TB GPU)
Storage 10 PB, 240 GB/sec peak data rate
Speed 17.59 PF @ Linpack)
27 petaFLOPS theoretical peak
Cost US$97 million

## Slide 21: Sunway TaihuLight - #1 @ 125/93 PF
Site: Nat. SC Center in Wuxi
Manufacturer: NRCPC
Cores: 10,649,600
Linpack Performance (Rmax) 93,014.6 TFlop/s
Theoretical Peak (Rpeak) 125,436 TFlop/s
Nmax 12,288,000
Power: 15,371.00 kW (Submitted)
Memory: 1,310,720 GB
Processor: Sunway SW26010 260C 1.45GHz
Interconnect: Sunway
Operating System: Sunway RaiseOS 2.0.5

## Slide 22: AMOS “Balanced” Cyberinstrument @ CCI
Blue Gene/Q
  ~1 PF peak @ 2+ GF/watt
  81,920 cores
  80 TB RAM
  More bandwidth than 1 million
  home ISP
Data Center Network
  IB FDR Switch
  324 ports @ 56 Gbit/sec each
Disk storage
  IBM Elastic Storage
  2 petabytes raw
  Bandwidth: 10 to 20 GB/sec
X86 clusters
  RSA: 34 nodes, 8 Xeon cores, 256GB RAM
  DRP: 64 nodes, 16 Xeon cores, 128GB RAM

## Slide 23: “Summit” DCS Supercomputer

## Slide 24: Disruptive Exascale Challenges…
1 billion-way parallelism
Cost budget of O($200M) and O(20M watts)
  Note: 1M watt per year == $1 million US dollars
Power
  500 pJ/op using Blue Gene/Q data
  Need 20 pJ/op ( ~50 GF/watt) to meet 20 Mwatt power ceiling
  Dominated by data movement & overhead
Programmability
  Writing an efficient parallel program is hard!
  Locality required for efficiency
  System complexity is BARRIER to programmability

## Slide 25: Power Drives Radically New Hardware and Software
Compute is FREE, cost is moving data
All software will have to be radically redesigned to be locality aware
Bill Dally – All CS complexity theory will need to be re-done!
Note: IBM Blue Gene/Q @ 45 nm!!

## Slide 26: History of Supercomputer Power & Price
Source: The Platform.Net
 20x larger version of AMOS
Notes: http://www.theplatform.net/wp-content/uploads/2015/04/hpc-over-time-table-3.jpg

## Slide 27: What are SC’s used for??
Can you say “fever for the flavor”..
Yes, Pringles used an SC to model airflow of chips as the entered “The Can”..
  https://www.hpcwire.com/2006/05/05/high_performance_potato_chips/
Improved overall yield of “good” chips in “The Can” and less chips on the floor…
P&G has also used SCs to improve other products like: Tide, Pampers, Dawn, Downy and Mr. Clean

## Slide 28: Patient Specific Vascular Surgical Planning
  Virtual flow facility for patient specific surgical planning
  High quality patient specific flow simulations needed quickly
  Simulation on massively parallel computers
  Cost only $600 in ‘09 on 32K Blue Gene/L vs. $50K for a repeat open heart surgery…
  At exascale this will cost more like 6 cents!
Notes: 28
Added reference to Simmetrix

## Slide 29: Operation “White Frost” from 2008
Notes: Planning done on Cray XT3, Red Storm. Dedicated time for 2 month. Used mix of ensemble and hero runs.

## Slide 30: Disruptive Opportunities @ 2^60
A radical new way to think about science and engineering
  Extreme time compression on very large-scale complex applications
  Materials, Drug Discovery, Finance, Defense, and Disaster Planning & Recovery…
Technology enabler for …
  Smartphone “supercomputers” w/ 25 GFlop and 100’s GB RAM
  Petascale “supercomputer” in all major universities @ $200K
  IBM Watson – AI/DL “desk-side” edition
  Home users have 100 GB network and Terascale+ “home” supercomputers…
  Exascale Neuromorphic procesors!!!